## Slide 1: DELETE THIS SLIDE PRIOR TO PRESENTATION
This PowerPoint serves as a template presentation which introduces topics related to air quality and is part of a suite of presentations provided by the EPA for the Megacities program.
See speaker notes for an additional description of slide content. Slides should be edited or added to as necessary for your particular needs. Slides with highlighted yellow text require the addition of specific context and information for your city.

## Slide 2: Source Apportionment

## Slide 3: Overview
1. Pollutant Sources
2. Positive Matrix Factorization
3. Using Source Apportionment in BenMAP Analyses

## Slide 4: Section 1: Pollutant Sources
1. Pollutant Sources
2. Positive Matrix Factorization
3. Using Source Apportionment in BenMAP Analyses

## Slide 5: Where Do Pollutants Come From?
Agriculture
Energy production
Natural sources
Waste (landfills)
Road transport
Fuel combustion (industry, households, others)

## Slide 6: Pollutant Types
Primary Pollutants
PM2.5:
Secondary Pollutants
PM2.5:
Air toxics
Benzene
PM₁₀: dust, ash, soot​
Ozone (O₃):
Black Carbon (BC)
Organic Carbon (OC)
Elemental Carbon (EC)
Sulfate (SO₄) ​
Toluene
Pesticides
Plasticizers
Sulfur dioxide (SO₂)
Volatile Organic Compounds (VOCs)
VOCs
Methane (CH₄)
NOx​
Nitrogen oxides (NOx)

## Slide 7: [YOUR CITY]: Pollution Sources
In this slide, include major sources of pollution in your city. If possible, please elaborate on the trends in pollution sources in following slides, i.e., changes in vehicle composition, decreases in solid waste burning, new industries or industry regulation
Example: Accra
  Crustal dust
  Biomass burning​
  Vehicle emissions​
  Tire and brake wear​
  Road dust​
  Sea salt​
  Solid waste burning
Harmattan winds
Traffic in Accra
Sea spray at Labadi beach

## Slide 8: [YOUR CITY]: Emissions Characteristics
Include elemental breakdown of pollution sources in your city if there is an existing study documenting source types and elemental composition of emissions.
Example: Accra
Source​ | Elemental species​
Crustal dust​ | Si, K, Ca, V, Cr, Ni, Cu, Fe, Ti, Al, Mg, Mn​
Biomass burning​ | K, Cl, SO4, Ca, P​
Aged biomass burning​ | K, SO4​
Sea salt​ | Na, Cl, S​
Vehicle exhaust/Road dust​ | Cu, Zn, Sb, Pb, Ni, Al, Si, Ca, Fe​
Solid waste burning​ | Br​
Gugamsetty et al. 2012, Zhou et al. 2013, Vossler et al. 2015, Zhou et al. 2014​
Notes: This information will need to come from a source apportionment study already completed in your city. Karagulian et al., 2015 may mention relevant studies. Conducting a literature search on articles related to your city and the terms “Source Apportionment,” “PMF,” or “chemical mass balance” may be helpful as well.

## Slide 9: [YOUR CITY]: Source Apportionment
If data is available, include overview of source apportionment in your city
Example: Accra
Zhou et al. 2013

## Slide 10: Source Apportionment Global Review
Karagulian et al., 2015

## Slide 11: Source Apportionment Global Review
Karagulian et al., 2015

## Slide 12: Source Apportionment Global Review
419 source apportionment studies in 51 countries analyzed ambient urban PM2.5 for its source
Add values of your city if applicable
Emissions Source | [YOUR CITY] | Globally
Traffic |  | 25%
Industrial activity |  | 15%
Domestic fuel burning |  | 20%
Sources of human origin (unspecified) |  | 22%
Natural sources (dust and sea salt) |  | 18%
Karagulian et al., 2015

## Slide 13: Source Apportionment
Best supported by gravimetric / filter samples that can be chemically analyzed to identify
  Organic constituents
  Metals
Use tools such as positive matrix factorization (PMF), chemical mass balance models (CMB), or the Unmix model to analyze speciated data, match sources and estimate contributions of each

## Slide 14: Bottom-Up and Top-Down Approaches to Air Quality
Adapted from Johnson et al. 2011 by Sonoma Technologies, Inc., used with permission.

## Slide 15: Receptor Models
f = species profile​
g = amount of mass contributed by each factor
e = error

## Slide 16: Receptor Models
knowledge about sources
none
complete
Multivariate
Receptor
Model
Chemical
Mass
Balance
Model
Explanatory Factor
Analysis Models
p is unknown
F is unknown
m > 1
Regression Models
p is known
F is known
m = 1
Confirmatory Factor
Analysis Models
p is hypothesized
F is partially known
m > 1
PMF
CMB
UNMIX
Notes: CMB can be applied to one sample, requires source profiles, effective near-source with well characterized source emissions. ​
UNMIX does not use uncertainty, so if no edge resolution, no solution is possible. Determines source contribution. ​
PMF does not need source profile, but needs a lot of ambient measurements, and sources must vary temporally to be resolved.
​
Chemical Mass Balance (CMB) Model​
Receptor model using effective-variance least squares method​
Requires speciated profiles of potentially contributing sources and corresponding ambient data from analyzed samples at a single receptor site​
Ideal for localized nonattainment problems ​
​
UNMIX Model​
Unmixes concentrations of chemical species measured in ambient air to identify contributing sources​
Chemical profiles of sources not required, instead are generated internally from ambient data using factor analysis​
Estimates number of sources, compositions, and contributions to each sample​
​
Positive Matrix Factorization (PMF)​
Mathematical receptor model ​
Analyzes environmental sample data​
Reduces large number of variables in complex analytical datasets to source types and contributions​
Can be used for many samples at many sites​
Provides robust uncertainty estimates and diagnostics

## Slide 17: Section 2: Example Tool: Positive Matrix Factorization
1. Pollutant Sources
2. Example Tool: Positive Matrix Factorization
3. Using Source Apportionment in BenMAP Analyses

## Slide 18: Positive Matrix Factorization (PMF)
Multivariate factor analysis tool
Decomposes matrix of speciated sample into factor contributions and factor profile matrices
Values must be positive (non-negative)
Inputs:
  Mass of each species in each sample
  Uncertainty of each species mass in each sample
Outputs:
  Source factor profiles
  Source contributions
Notes: The goal of receptor models such as PMF is to solve the chemical mass balance between measured species concentrations and source profiles, with the number of factors, the species profile of each source, and the amount of mass contributed by each factor to each individual sample.
Inputs to PMF include the mass of each species in a sample, which comes from a filter measurement that is then speciated in a lab setting into its component parts, and the uncertainty of each species in each sample.
Outputs include the source factor profiles, or fingerprints of each source type, and the relative contribution of each source to the total mass. Note that SPECIES (e.g., Pb, Si) are not the same as the sources (e.g., road dust, sea salt).

## Slide 19: PMF Basics
Goal is to solve the chemical mass balance between measured species concentrations and source profiles
f = species profile​
g = amount of mass contributed by each factor​
PMF decomposes a matrix of speciated sample data into factor contributions (G) and factor profiles (F)
Factor profiles must be interpreted by the user to identify the source types contributing to that factor

## Slide 20: PMF Calculations
Xij = Matrix of observations on i days for j species
Gik = Factor contributions on day i for factor k
  Units of ng/m3 / m3
Fkj = Factor compositions to factor k for species j
    Units of ng/ng
p = Number of factors (user selected)
Date EC_ng/m3 OC_ng/m3…. Species_J
Day_1 120.0 1040.0 ……..
Day_2 197.0 1320.0 ..…..
. . .
. . .
. . .
Factor EC OC …… Species_J
Factor1 234.1 1410.0……..
Factor2 237.0 5334.0..…..
Factor3 . .
. . .
Factor_P . .
Date Factor1 Factor2…. FactorP
Day_1 120.0 1040.0 ……..
Day_2 197.0 1320.0 ..…..
. . .
. . .
Day_i . .
i days
i days
p factors
j species

## Slide 21: PMF Fundamentals
PMF 5.0 Fundamentals and User Guide
Displacement

## Slide 22: EPA’s PMF Tool Process
Input Data
Data diagnostics
Base model run 1
Base model run diagnostics
Base model run 2
Source factor profile analysis

## Slide 23: Step 1. Input Data

## Slide 24: Monitoring Sites

## Slide 25: Getting Started with PMF
Sample species concentrations
Sample species uncertainty values
https://www.epa.gov/air-research/positive-matrix-factorization-model-environmental-data-analyses

## Slide 26: Concentration Files
Headers for both sheets must be identical; can’t have spaces
Missing data must be listed as -999
During file preparation, remove species with more than 50% of samples missing or below detection limit
Uncertainty files can be observation-based or equation-based
Concentration file
Uncertainty file

## Slide 27: Input Data

## Slide 28: Input Data

## Slide 29: Step 2. Data Diagnostics

## Slide 30: Weighting Species

## Slide 31: Descriptive Data
Concentration Scatter Plot
Concentration Time Series
Data exceptions

## Slide 32: Step 3. Base Model 1

## Slide 33: Base Model Run
Choose Random Start
Select number of factors
Select number of runs

## Slide 34: Base Model Run
Q (Robust) and Q (True) are goodness-of-fit parameters that assess how well the model fits the input data.
Lowest Q (Robust) is model run that is depicted.

## Slide 35: Step 4. Base Model Diagnostics

## Slide 36: Residual Analysis
Uncertainty-scaled residuals
Shows how well the model fits each species
If a species has many large scaled residuals, this indicates poor model fit
Residuals should be within +3 and -3

## Slide 37: Observed/Predicted Scatter Plot
Comparison between observed (input data) and predicted (modeled) values used to determine if the model fits the individual species well
Species that do not have a strong correlation between observed and predicted should be downweighted

## Slide 38: Step 5. Base Model Run 2

## Slide 39: Re-Running the Base Model
Re-run base model based on decisions made from residual analysis and predicted v. observed scatter plots
Use the same base model run starting point:
  20 runs
  6 factors
  Random start
Next, re-check the residual analysis and predicted v. observed figures

## Slide 40: Step 6. Source Factor Profile Analysis

## Slide 41: Profile/Contributions: Solid Waste Burning

## Slide 42: Profile/Contributions: Sea Salt

## Slide 43: Profile/Contributions: Crustal Dust

## Slide 44: Profile/Contributions: Aged Biomass

## Slide 45: Profile/Contributions: Road Dust

## Slide 46: Profile/Contributions: Biomass Burning

## Slide 47: Factor Fingerprints

## Slide 48: Factor Contributions

## Slide 49: Output Files
File Name | Contents
*_diag | record of the user inputs and model diagnostic information (identical to the Diagnostics screen)
*_contrib | Contributions for each base run used to generate the contribution graphs on the Profiles/Contributions tab. Sorted by run number
*_profile | Profiles for each base run used to generate the profile graphs on the Profiles/Contributions tab.
*_resid | Residuals (regular and scaled by uncertainty) for each base run, used to generate the graphs and tables on Residual Analysis screen
*_run_comparison | Summary of the species distribution for each factor over all PMF runs and compared to lowest Q(robust) run
*_base | Contrib, Profile, Resid, and Run Comparison on separate worksheets in the same excel workbook.

## Slide 50: Next Steps in PMF
After running the base model, you can:
  Re-run the base model for a different number of factors to see if another value has a better fit to input data
  Estimate displacement error
  Estimate base model error
EPA PMF has a number of training exercises associated with it that can be used for practicing the technique and understanding source profiles
Many studies can be used to understand source profiles, as well

## Slide 51: How to Use PMF Results
Once you have run PMF and are confident in the source contributions and their profiles, you can use this information in a number of ways:
  Understanding individual source contributions overall and by neighborhood
  Air quality control strategy creation
  Policy assessment
  Creating a baseline for future analyses

## Slide 52: After Using PMF
Trend analyses by contributions
  Day of week vs. weekday box plots or non-parametric tests
  Spectral analysis to find periodicity
  Seasonal analysis
  Contribution by wind speed and direction
    Nonparametric regression (NPR)
Mass apportionment
    Can include total mass directly as a species to get mass apportionment (Reff et al., 2007)
    Multiply out the factor profiles and contributions to get mass from each factor

## Slide 53: Section 3: Using Source Apportionment in BenMAP Analyses
1. Pollutant Sources
2. Positive Matrix Factorization
3. Using Source Apportionment in BenMAP Analyses

## Slide 54: Environmental Benefits Mapping and Analysis Program (BenMAP) Analysis Outline
Example is for Accra:
  Air pollution sources in Accra
  Source apportionment study in Accra
Using source apportionment data to create targeted monitor rollback scenario in BenMAP
Health incidence results from targeted monitor rollback
Comparing source apportionment monitor rollback results with baseline assessment results
Note that the analysis done during this exercise is simplified for illustrative purposes and does not reflect an actual policy proposed by Ghana.

## Slide 55: Using Source Apportionment Details in BenMAP
Monitor Site (24-hour average) | Total PM2.5 (µg/m3) | Road dust & vehicle (µg/m3) | Fresh & Aged Biomass (µg/m3)
Jamestown | 57 | 5 (8.8%) | 21 (36.8%)
Asylum Down | 31 | 10 (32.3%) | 10 (32.3%)
Nima – 1 | 33 | 8 (24.2%) | 12 (36.4%)
Nima – 2 | 37 | 11 (29.7%) | 13 (35.1%)
East Legon | 28 | 3 (10.7%) | 11 (39.3%)
Note these are 24-hour average measurements taken during non-Harmattan season,
whereas other monitoring may include all months of the year.
Zhou et al., 2013

## Slide 56: Analytical Assumptions
We assume 1:1 correspondence between the percent reduction in PM2.5 emissions in a source category and percent reduction in ambient PM2.5 concentrations from that category
We assume full compliance with the hypothetical regulation (e.g., full 50% decrease in source-specific PM2.5 concentration)
We assume full implementation of the hypothetical regulation by 2020

## Slide 57: Source Apportionment in Accra
Monitor Site (24-hour average) | Total PM2.5 (µg/m3) | Road dust & vehicle (µg/m3) | Fresh & Aged Biomass (µg/m3) | Total Road and Biomass (µg/m3) | Decrease Road and Biomass Emissions by 50% - Decrease total PM2.5 by:
Jamestown | 57 | 5 (8.8% of total) | 21 (36.8% of total) | 26 (45.6% of total) | 22.8%
Asylum Down | 31 | 10 (32.3% of total) | 10 (32.3% of total) | 20 (64.5% of total) | 32.3%
Nima – 1 | 33 | 8 (24.2% of total) | 12 (36.4% of total) | 20 (60.6% of total) | 30.3%
Nima – 2 | 37 | 11 (29.7% of total) | 13 (35.1% of total) | 24 (64.9% of total) | 32.4%
East Legon | 28 | 3 (10.7% of total) | 11 (39.3% of total) | 14 (50.0% of total) | 25.0%
Zhou et al. 2013
Notes: At each monitoring site, we show the PM2.5 attributable to each source according to the PMF analysis in Zhou et al., 2013. In the final column, we see that if we decrease road and biomass emissions by 50%, this decreases total PM2.5 by different percentages, as shown in the red box.

## Slide 58: Applying Reductions by Monitor
East Legon
Nima
Asylum Down
Jamestown
Zhou et al., 2013
Notes: We apply reductions in PM concentrations to the monitors in each neighborhood, as shown in the figure on the left. The figure on the right shows the percent of households in Accra using biomass fuels, with the brightest green referring to lower percentages, and darker reds referring to higher percentages.

## Slide 59: Monitor Rollback Scenario
Region | Percent
1, East Legon | 25.0
2, Nima | 31.4
3, Asylum Down | 30.0
4, Jamestown | 22.8
BenMAP-CE monitor rollback scenario screenshot
Notes: We use BenMAP-CE to analyze the policy scenario laid out two slides prior. We apply the percent reduction in PM2.5, shown in the table on the right, to the spatial areas aligned with the regions in the BenMAP screenshot on the left.

## Slide 60: Monitor Rollback Scenario
Change in PM2.5 concentrations across Accra associated with emissions reduction policy scenario, in µg/m3
Notes: Change in PM2.5 concentrations across Accra due to emissions reduction policy scenario

## Slide 61: Health Impact Results: US-Based Studies
Health Endpoint | Epidemiological Study | Age Range | Change in Incidence due to 2020 Targeted Mitigation Rollback
Mortality, All Cause | Krewski et al. 2009 | 30-99 | 3,607
Mortality, All Cause | Laden et al. 2006 | 25-99 | 8,428
Mortality, All Cause | Pope et al. 2002 | 30-99 | 3,607
Health Endpoint | Epidemiological Study | Age Range | Change in Incidence due to 2020 Targeted Mitigation Rollback
Mortality, All Cause | Woodruff et al. 1997 | Infants | 143
Mortality, All Cause | Woodruff et al. 2006 | Infants | 235
Notes: Note: Update results with appropriate significant figures based on data inputs.

## Slide 62: Health Impact Results: Integrated Exposure Response Function (IER)
Health Endpoint | Epidemiological Study | Age Range | Change in Incidence due to 2020 Targeted Mitigation Rollback
Mortality, Ischemic Heart Disease | Burnett et al. 2014 | 30-99 | 542
Mortality, Cerebrovascular Disease | Burnett et al. 2014 | 30-99 | 1,049
Mortality, COPD | Burnett et al. 2014 | 30-99 | 51
Mortality, Lung Cancer | Burnett et al. 2014 | 30-99 | 21

## Slide 63: Health Impact Results: Asthma Hospital Admissions
Health Endpoint | Epidemiological Study | Age Range | Change in Incidence due to 2020 Targeted Mitigation Rollback
Hospital Admissions, Asthma | Sheppard et al. 2003 | 0-64 | 168,937

## Slide 64: Comparison with Baseline Assessment
What do these results mean?
  How do these results compare with the baseline assessment results?
  Why did you use 2020 projected air quality data instead of 2014 monitored air quality data?

## Slide 65: 2020 Health Impact Results: US-Based Studies
Health Endpoint | Epidemiological Study | Age Range | 2020 PM2.5 Attributable Incidence | Change in Incidence due to 2020 Targeted Mitigation Rollback | Incidence Post-Rollback
Mortality, All Cause | Krewski et al. 2009 | 30-99 | 10,430 | 3,607 | 6,823
Mortality, All Cause | Laden et al. 2006 | 25-99 | 17,711 | 8,428 | 9,283
Mortality, All Cause | Pope et al. 2002 | 30-99 | 10,430 | 3,607 | 6,823
Health Endpoint | Epidemiological Study | Age Range | 2020 PM2.5 Attributable Incidence | Change in Incidence due to 2020 Targeted Mitigation Rollback | Incidence Post-Rollback
Mortality, All Cause | Woodruff et al. 1997 | Infants | 452 | 143 | 309
Mortality, All Cause | Woodruff et al. 2006 | Infants | 663 | 235 | 428

## Slide 66: 2020 Health Impact Results: IER
Health Endpoint | Epidemiological Study | Age Range | 2020 Air Pollution Attributable Incidence | Change in Incidence due to 2020 Targeted Mitigation Rollback | Incidence Post-Rollback
Mortality, Ischemic Heart Disease | Burnett et al. 2014 | 30-99 | 1,487 | 542 | 945
Mortality, Cerebrovascular Disease | Burnett et al. 2014 | 30-99 | 2,140 | 1,049 | 1,091
Mortality, COPD | Burnett et al. 2014 | 30-99 | 155 | 51 | 104
Mortality, Lung Cancer | Burnett et al. 2014 | 30-99 | 60 | 21 | 39

## Slide 67: 2020 Health Impact Results: Asthma Hospital Admissions
Health Endpoint | Epidemiological Study | Age Range | 2020 Air Pollution Attributable Incidence | Change in Incidence due to 2020 Targeted Mitigation Rollback | Incidence Post-Rollback
Hospital Admissions, Asthma | Sheppard et al. 2003 | 0-64 | 537,805 | 168,937 | 368,868

## Slide 68: Thank you!